| Symbol | Description | Parent Material | Physiographic element | Vegetation | Topography Slope | Soil Texture Topsoil Subsoil | Depth (cm) | Soil Ph Top soil Subsoil | Organic Matter (%) topsoil | Drainage | Classification | Limitations (theoretical) for rain fed agriculture | Limitations (theoretical) for irrigated rice |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  |  |  |  |  |  |  |  | USDA (1990) | FAO (1974) |  |  |
| Alluvial and colluvial zones in lowlands and depressions (A, BC, G, R, RC, TNH) |
| Al | Light textured soils, yellow-grayish very deep and mottled | Recent alluvial deposits | In alluvial plains, along rivers and streams | Forest, groves, prairie and cultures (fruit orchards, annual crops, timber) | Flat or mostly flat 0 - 2 | Sandy-loam Sandy-loam to sandy= | >180 | 6.2 - 7.8 6.4 - 8.0 | 0.9 - 2.7 | Well drained to excessively drained | Ustifluvents | Fluvisols Kastanozems | Low fertility, low water holding capacity, sub-optimal drainage, sometimes has deficiency in Zn and Fe (high pH) | Too rapid infiltration, compaction risks, low fertility, sometimes deficient in Fe when Aerobic and Zn when Anaerobic |
| Alp | Light textured soils, rocky, yellowish or reddish gray, deep |  |  |  | Flat to slightly undulating 0 – 3 | Sandy-loam Sandy-loam to sandy | >100 | 6 - 6.5 5 - 7 |  | Well drained |  |  | Low fertility, low water holding capacity, sub-optimal drainage, rocky, sometimes has deficiency in Zn and Fe (high pH) | Too rapid infiltration, compaction risks, low fertility, rocky, sometimes deficient in Fe when Aerobic and Zn when Anaerobic |
| Am | Medium textured soils, yellowish or dull orange-grayish, very deep and mottled |  |  |  | Flat 0 - 1 | Loam to Sandy-clay-loam Loam to silty-clay-loam | >180 | 6.1 - 7.2 6.5 - 7.7 | 1.4 - 3.1 | Moderately well drained to poorly drained | Tropofluvents | Fluvisols Kastanozems | Sub-optimal drainage, unfavorable to germination, sometimes low fertility, liming required or need to use Al adapted species. | Sub-optimal infiltration, compaction risk, sometimes low fertility |
| Amp | Yellowish alluvial soil, deep and mottled, medium texture, rocky phase |  |  |  | Flat to slightly undulating 0 - 3 | Sandy-loam Sandy-clay |  |  |  | Well drained to moderately well drained |  |  | Unfavorable to germination, rocky, sometimes low fertility, liming required or need to use Al adapted species. | Sub-optimal infiltration, compaction risk, rocky, sometimes low fertility |
| Ap | Heavy soil, yellowish, grayish and greenish, very deep |  |  |  | Flat 0 - 1 | Silty-loam to clay Silty-loam to clay | >180 | 6.1 - 8.1 6.4 - 8.7 | 1.6 - 5.3 | Well drained to moderately well drained |  | Fluvisols Kastanozems Cambisols | Soil compaction risk, Zn and Fe deficiency risk (High pH), and sometimes low fertility. | Weak soil structure, deficient in Fe when Aerobic and Zn when Anaerobic, sometimes low fertility |
| Apt | Heavy soil, yellowish, grayish and greenish, very deep and mottled |  |  |  |  |  |  |  |  | Imperfectly drained to poorly drained |  |  | Soil compaction risk, Zn and Fe deficiency (High pH), inadequate drainage, sometimes low fertility. |  |
| Apd | Heavy soil, yellowish, grayish and greenish, shallow and mottled |  |  |  |  |  | 70 - 120 |  |  | Well drained to moderately well drained | Ustifluvents |  | Soil compaction risk, Zn and Fe deficiency (High pH), and sometimes low fertility. |  |
| A3 | See above (A soils) |  |  |  | See above (A soils) |
| Acl | Calcareous soil, light texture, brown to grayish, very deep and mottled | Recent alluvial deposits over limestone |  | Forest, groves, savannah and orchards (coffee and fruit trees) | Flat 0 - 1 | Sandy-loam Loamy-sand | >180 | 8.1 - 8.8 8.0 - 8.5 | 1.2 - 4.1 | well drained | Ustifluvents | Calcaric Fluvisols | Sub-optimal drainage, low fertility, high pH induces deficiencies in Fe and Zn | Too rapid infiltration, compaction risk, low fertility, deficient in Fe when Aerobic and Zn when Anaerobic (high pH) |
| Alcp | Calcareous soil, light texture, rocky, brown to grayish, deep and mottled |  |  |  |  | Sandy-loam Loamy-sand | >100 | 8.0 - 8.5 7.5 - 8.0 | 1.5 - 3.5 | well drained |  |  | Rocky, sub-optimal drainage, low fertility, high pH induces deficiencies in Fe and Zn | Rockiness, too rapid infiltration, compaction risk, low fertility, deficient in Fe when Aerobic and Zn when Anaerobic (high pH) |
| Amc | Calcareous soil, heavy texture, yellowish to dull orange, very deep and mottled |  |  |  |  | Sandy-loam to clay-loam Sandy-loam | >180 | 8.1 - 8.8 8.0 - 8.4 | 1.2 - 4.6 | Moderately well drained to poorly drained |  | Fluvisols fluvicalcic Kastanozems | Unfavorable to germination, sub-optimal drainage, high pH induces deficiencies in Fe and Zn | Sub-optimal infiltration, compaction risk, sometimes low fertility, deficient in Fe when Aerobic and Zn when Anaerobic (high pH) |
| Apc | Calcareous soil, heavy texture, grayish to greenish, very deep and sometimes mottled | Recent alluvial deposits over limestone | In alluvial plains, along rivers and streams | Forest, groves, savannah and orchards (coffee and fruit trees) | Flat 0 - 1 | Silty-clay to clay Clay | >180 | 7.8 - 8.5 7.5 - 8.9 | 2.0 - 5.6 | Imperfectly drained to poorly drained | Ustifluvents | Fluvisols fluvicalcic Kastanozems | Compaction risk when tilled while moist, sub-optimal drainage, high pH induces deficiencies in Fe and Zn | weak soil structure, deficient in Fe when Aerobic and Zn when Anaerobic, sometimes low fertility |
| Apch | Calcareous soil, heavy texture, grayish to greenish, very deep and very mottled |  |  |  |  |  |  |  |  | Poorly drained |  |  | Compaction risk when tilled while moist, necessary drainage, high pH induces deficiencies in Fe and Zn |  |
| A2 | See above (Ac) | Recent alluvial deposits over limestone | In alluvial plains, along rivers and streams | Forest, groves, savannah and orchards (coffee and fruit trees) | See above (soils At) |
| A1 | See above (Ac) |  |  |  |  |
| Ate | Variable texture, brown to grayish, very deep (thick) | Old alluvial deposits | Plateaux , Fluvial terraces and along rivers | Forest, prairie, orchards (fruit trees) | Almost flat to slightly undulated 1 -3 | Variable | >180 | 5.1 - 7.0 5.2 -7.8 | 0.5 - 3.3 | Well drained to imperfectly drained | Tropofluvents | Fluvisols Kastanozems Cambisols | Variable (see Atl, Atm, Atp |
| Atd | Variable texture, brown to grayish, shallow |  |  |  |  |  | <50 |  |  |  |  |  | Erosion risks when sloping | Limiting depth |
| Atdp | Variable texture, brown to grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risks when sloping, rocky soil | Limiting depth, rocky soil |
| Ath | Variable texture, grayish and very mottled |  |  |  |  |  | >180 |  |  | Poorly drained |  |  | Erosion risks when sloping, drainage needed | Variable (see Atl, Atm, Atp) |
| Atl | Light texture soil, brown to grayish, deep |  |  |  |  | Sandy-loam Sandy-loam | >100 | 6.0 - 7.0 6.2 - 7.2 |  | well drained |  | Fluvisols | Low water holding capacity | Sub-optimal infiltration, inadequate texture, compaction risk |
| Atm | Medium textured soil, dull orange to reddish, very deep and mottled |  |  |  |  | Sandy loam to clay-loam Sandy-loam to clay | >180 | 5.1 - 6.0 5.2 - 7.8 |  | Well drained to imperfectly drained |  | Fluvisols Kastanozems Cambisols | Low fertility, sometimes liming required or need to use Al adapted species, rocky soil | Low fertility, sometime very rocky |
| Atp | Heavy textured soil, grayish to brownish, very deep and mottled |  |  |  | Flat to almost flat 0 - 2 | Clay-loam to clay Clay-loam to clay |  | 5.4 -6.9 5.2 - 6.6 | 2.2 - 3.9 | Poorly drained |  | Fluvisols Kastanozems | Compaction risks when till while moist, Al toxicity, drainage necessary | Possibility to form a mud with no porosity. Al toxicity when aerobic |
| AT | See above (soils At) |  |  |  | See above (soils At) |
| Atec | Calcareous soil, variable texture, grayish and very deep |  |  | Savannah and prairies. Sometimes cactuses | Flat 0 - 1 | Variable | >180 | 7.6 - 8.6 7.7 - 8.7 | 0.7 - 2.4 | Variable | Ustifluvents | Kastanozems Fluvisols | Variable (see Atlc, Atpc) |
| Atdc | Calcareous soil, variable texture, grayish and shallow |  |  |  |  |  | <50 |  |  |  |  |  | Variable (see Atlc, Atpc), limiting depth |
| Atdpc | Calcareous soil, variable texture, grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Variable (se Atlc, Atpc), limiting depth, rocky |
| Atlc | Calcareous soil, light texture, grayish and very deep | Old alluvial deposits | Plateaux , Fluvial terraces and along rivers | Savannah and prairies. Sometimes cactuses | Flat 0 - 1 | Sandy-loam Loamy-sand | >180 | 7.6 - 8.6 7.7 - 8.7 | 0.7 - 1.5 | Excessively drained to well drained | Ustifluvents | Kastanozems | Low water holding capacity, sub-optimal drainage, low fertility, possible deficiency in Fe and Zn (high pH) | Compaction risks, rapid infiltration. Low fertility, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| Atpc | Calcareous soil, heavy structure, grayish or yellowish, very deep |  |  |  |  | Clay Clay-loam to clay |  | 7.9 - 8.5 7.9 - 8.2 | 1.8 - 2.4 | Poorly drained |  | Fluvisols Kastanozems | Drainage necessary, low fertility, compaction risk when tilled while moist, deficiency in Fe and Zn (high pH) | Possibility to form a mud without porosity. Low fertility, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| BCl | Light texture, grayish or greenish, very deep | Colluvial deposits | Depressions and lowlands on hill bases or along water courses in the North coast | Forest, groves, savannah, prairies and crops (fruit trees, annual crops, forestry) | Flat 0 - 1 | Sandy-loam Loamy-sand to sandy-loam | >180 | 6.2 - 7.2 6.7 - 7.7 | 1.0 - 3.5 | Well drained | Tropofluvents | Fluvisols | Low water holding capacity, low fertility | Sub-optimal infiltration, inadequate texture |
| BC2 | Similar to BCl, however has better drainage |  |  |  |  |  |  |  |  | Well drained to excessively drained |  |  |  |  |
| BClp | Light textured soil, grayish or greenish, very deep and rocky |  |  |  |  |  |  |  |  | well drained |  |  | Rocky, low water holding capacity, low fertility | Rocky, sub-optimal infiltration, inadequate texture |
| BCm | Medium textured soil, grayish, dull orange or yellowish, deep |  |  |  |  | Sandy-loam to clay-loam Sandy-loam to clay-loam | >150 | 6.2 - 7.8 6.3 - 7.9 | 1.2 - 3.6 | Well drained to moderately well drained |  | Fluvisols Kastanozems | Low fertility, sometimes unfavorable to germination and or Zn and Fe deficiency (high pH) | Sub-optimal texture, compaction risk, low fertility, sometimes deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| BCp | Heavy textured soil, grayish to yellowish, mottled, very deep |  |  |  |  | Clay-loam to clay Clay-loam to clay | >180 | 6.2 - 7.0 7.1 - 7.2 | 4.3 - 6.3 | Imperfectly drained to poorly drained |  | Kastanozems | Compaction risk when tilled while moist, sub-optimal drainage, sometimes manual till difficult (vertic soil) | Risk of cracking strongly when dry and possible formation of a mud without pores. Possible P deficiency |
| BCph | Heavy textured soils, black or greenish, hydromorphic and very deep |  |  |  |  | Clay Clay |  | 6.1 - 6.8 6.7 - 7.4 | 2.1 - 4.2 | Very poorly drained | Tropaquents | Gleysols | Rain fed agriculture non adapted, compaction risks when till while moist | Possible deficiency in Zn when submerged for long time. |
| BC1 | Similar to non calcareous BC soils |  |  |  |  | See soils BC non calcareous |
| BClc | Light texture, grayish, yellowish or greenish, deep | Calcareous colluvial deposits |  |  |  | Loamy-sand to sandy-loam Sandy-loam to sandy-clay-loam | >150 | 7.6 - 8.0 8.2 - 8.6 | 0.9 - 3.0 | Well drained | Ustifluvents | Fluvisols | Possible deficiency in Zn and Fe (high pH), sometimes unfavorable to germination and low Cation Exchange Capacity | Compaction risks or inadequate texture, deficiency of Fe when aerobic and Zn when anaerobic (high pH), sometimes weak Cation Exchange Capacity |
| BClpc | Calcareous, light texture, grayish, yellowish or greenish, deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Rocky soils, possible deficiency in Zn and Fe (high pH), sometimes unfavorable to germination and low Cation Exchange Capacity | Rocky, compaction risks or inadequate texture, deficiency of Fe when aerobic and Zn when anaerobic (high pH), sometimes weak Cation Exchange Capacity |
| BCmc | Calcareous soil. Medium texture, grayish or yellowish, very deep |  |  |  |  | Sandy-loam to sandy-clay-loam Sandy-loam to sandy-clay-loam | >180 | 8.2 - 8.5 6.8 - 8.6 | 1.7 - 3.0 | Well drained to moderately well drained |  |  | Possible deficiency in Zn and Fe (high pH) | Compaction risks, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| BCpc | Calcareous soil. Heavy texture, yellowish or grayish or greenish, very deep |  |  |  |  | Silty-clay to clay Silty-clay to clay |  | 6.7 - 8.1 7.9 - 9.1 | 2.3 - 3.9 | Poorly drained |  | Fluvisols Kastanozems fluvicalcic | Drainage necessary, compaction risks when till while moist, Possible deficiency in Zn and Fe (high pH) | Possibility to form a pore less mud, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| BCphpc | Calcareous soil. Heavy texture, yellowish, grayish or greenish, hydromorphic, very deep and rocky | Calcareous colluvial deposits | Depressions and lowlands on hill bases or along water courses in the North coast | Forest, groves, savannah, prairies and crops (fruit trees, annual crops, forestry) | Flat 0 - 1 | Clay Clay to clay-loam | >180 | 6.6 - 7.3 7.4 - 8.3 | 3.7 - 7.1 | Very poorly drained | Tropaquents | Gleysols | Rain fed agriculture non adapted, compaction risks when till while moist, commonly have Zn and Fe deficiency (high pH) | Possibility to form a pore less mud, possible Zn deficiency when subject to prolonged submersion |
| G | Gleyic soil (hydromorphic, medium to heavy texture, grayish, yellowish or olive, very deep and rocky) | Colluvial deposits, calcareous or non calcareous alluvial deposits | Depressions and flat lowlands | prairies and cultures (fruit trees, vegetable gardens, timber) | Flat 0 - 1 | Loam to clay Loam to clay | >180 | 6.5 - 7.1 7.0 - 7.9 (non calcareous G) 7.1 - 8.5 7.9 - 8.7 (calcareous G) | 1.9 - 7.2 |  |  |  | Rain fed agriculture non adapted, compaction risks when tilled while moist, low fertility, sometimes Zn and Fe deficiency and rockiness can be a limiting factor. | Low fertility, possible formation of a pore less muddy layer, possible deficiency in Fe and Zn when submerged for prolonged periods. Rockiness can be a limiting factor. |
| R | Sandy soil, brownish or yellowish. Variable depth | Sandy detrital deposits | Flat lowlands and dunes zones | Coconut groves and cactuses | Flat to slightly undulating 1 - 3 | Sandy Sandy | >50 | 5.9 - 6.9 5.9 - 6.9 | 1.9 - 2.9 | Well drained to excessively drained | Ustipsamments | eutric psamitic Regosols | Low water holding capacity, low fertility | Inadequate texture, infiltration rates to high. |
| RC | Calcareous soil, light to medium texture, brownish or yellowish, variable depth | Calcareous sandy detrital deposits | Flat areas in the along North Coast | Cactuses or no vegetation | Flat 0 - 1 | Sandy-loam Sandy to sandy-loam | >50 | 7.9 - 8.5 7.9 - 9.5 |  |  |  | psamitic Regosols | Low water holding capacity, low fertility, possible deficiency of Fe and Zn when (high pH) |  |
| TNH | Organic soil, black, variable depth | Lacustrine limestone | Depressions | Forest | Flat 0 - 1 | Organic | >30 | 7.1 - 7.5 7.1 - 7.5 | 20 - 80 | Imperfectly drained to poorly drained | Troposaprists Tropohemists | Histosols | Inadequate physical support, necessary drainage, commonly deficient in Zn and Fe and or limiting depth | Little or no potential due to soil organic nature. |
| TNHd | Organic soil, black, shallow |  |  |  |  |  | <30 |  |  |  |  |  |  |  |
| Mountain areas with plateaux and hilsides (CE, CQm PF, CFD, CD, CN, TN) |
| CE | Medium to heavy textured soils, yellowish, grayish or brown. Moderately deep | Weathered greywacke | Hillsides and steep slopes in mountain areas | Secondary forests, scrublands and crops (coffee) | hilly 15 - 30 | Silty-loam to clay Clay | 50 - 150 | 4.9 - 7.0 4.7 - 6.6 | 1.9 - 6.4 | Variable | Tropopsamment | Luvisols Regosols Acrisols | Compaction risk when tilled while moist, low fertility, sometimes liming required for almost all crops (extremely acidic soil), unfavorable germination | Limiting topography, possible formation of a pore less mud, low fertility |
| CEp | Medium to heavy textured soils, yellowish, grayish or brown. Moderately deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, low fertility, sometimes liming required for almost all crops (extremely acidic soil), unfavorable germination | Limiting topography, possible formation of a pore less mud, low fertility, rockiness |
| CEd | Medium to heavy textured soils, yellowish, grayish or brown. Shallow |  |  |  |  | Silty-loam to clay Bedrock | 30 - 50 |  |  | Well drained |  | Lithosols | High erosion risks, rocky outcrops, low fertility, compaction risks when tilled while moist | Limiting topography, none or low potential due to limiting depth and or rockiness and rocky outcrops. |
| CEdp | Medium to heavy textured soils, yellowish, grayish or brown. Shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | High erosion risks, rocky outcrops, low fertility, rockiness, compaction risks when tilled while moist |  |
| CQ | Medium textured soil, yellowish or brown, shallow and rocky | Weathered clay quartzite | Hills and slopes in North coast with many rock outcrops | low open scrublands | Mountainous | Sandy-loam Loam | 30 - 50 | 5.5 - 6.5 5.2 - 6.2 | 2.6 - 4.6 | Well drained to moderately well drained | Ustipsamments | Lithosols Kastanozems | High erosion risks, rockiness, rock outcrops, limiting depth, low fertility |  |
| PF | Medium to heavy textured soil, yellowish or brownish, moderately deep to very deep, mottled | Tutuala and Fato Limestone (dolomitic limestone, conglomerate and breccias) | Abrupt calcareous mountains | Forests, groves and savannah | Mountainous | Clay-loam to clay Clay | >80 | 5.1 - 7.2 5.0 - 6.6 | 4.0 - 11.0 | Moderately well drained to imperfectly drained | Dystropepts | Luvisols Cambisols | Rock outcrops, compaction risks when tilled while humid, low fertility, sometimes liming needed for acidity sensitive crops | Limiting topography, rock outcrops, possible formation of pore less mud and or rockiness |
| PFp | Medium to heavy textured soil, yellowish or brownish, moderately deep to very deep, mottled, rocky |  |  |  |  |  |  |  |  |  |  |  | Rock outcrops, rockiness, compaction risks when tilled while humid, low fertility, sometimes liming needed for acidity sensitive crops |  |
| PFd | Heavy textured soil, yellowish to brownish, shallow |  |  |  |  | Clay Clay | 30 - 80 |  |  | Well drained to moderately well drained |  | Rendzinas, calcaric Lithosols, calcaric Regosols | Extremely high erosion risks, soil depth, low fertility | Limiting topography and soil depth, rock outcrops, possible formation of a pore less mud, rockiness and low fertility. |
| PFdp | Medium to heavy textured soil, yellowish or brownish, shallow |  |  |  |  |  |  |  |  |  |  |  | Extremely high erosion risks, rockiness, soil depth, low fertility |  |
| CFD | Variable texture soil, brownish to yellowish, not very deep | Limestone and calcareous sandstones in association with brown clay and volcanic tuff |  | not specified |  | Variable |  | Variable | Variable |  |  | Lithosols | Extremely high erosion risks, low fertility |  |
| CFDp | Variable texture soil, brownish to yellowish, not very deep and rocky |  |  |  |  |  | 0 -30 |  |  |  |  |  | Extremely high erosion risks, soil depth, low fertility |  |
| CFDdp | Variable texture soil, brownish to yellowish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Extremely high erosion risks, rockiness, soil depth, low fertility |  |
| CDdp | Medium textured soil, dark brown, shallow and rocky | Acidic volcanic rocks | Mountains | Groves and savannah, natural pastures, crops (Fruit trees and vegetable gardens) |  | Sandy-clay-loam to clay Sandy-loam | 30 - 50 | 6.3 - 7.3 6.4 - 7.4 | 2.4 - 3.4 | Well drained | Haplumbrepts | Rankers | Erosion risk, soil depth, low fertility | Limiting topography and soil depth, compaction risk, low fertility |
| CPdp | Medium textured soil, brown or reddish, shallow and rocky |  |  | Forest |  | Clay-loam bedrock |  | 4.7 - 5.3 - | 5 - 11.0 | Well drained |  |  | Erosion risk, soil depth, liming necessary for sensitive crops. | Limiting topography and soil depth, low fertility |
| CN | Eroded soil, heavy texture, olive to grayish and sometimes mottled, very deep | Clay deposits, non-consolidated. Plenty of rocks from several origins | watersheds and depressions surrounded by mountainous terrain | Savannah and degraded pastures | Flat to undulated 0 - 8 | Clay Clay | >180 | 6.1 - 7.8 7.3 - 8.8 | 1.8 - 7.8 | Moderately well drained to poorly drained | Pelluderts | Vertisols, vertic Kastanozems | Compaction risk when tilled while moist, sub-optimal drainage, sometimes manual till difficult (vertic soil), Possible deficiency in Zn and Fe (high pH) | Possible formation of a pore less mud, possible P deficiency, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| CNp | Eroded soil, heavy texture, black, yellowish or olive, sometimes mottled, very deep and rocky |  |  |  | Flat to strongly undulated 0 - 15 |  |  |  |  | Imperfectly drained to poorly drained |  | Vertisols, Cambisols, Luvisols and vertic Kastanozems | Compaction risk when tilled while moist, sub-optimal drainage, rockiness, sometimes manual till difficult (vertic soil), Possible deficiency in Zn and Fe (high pH) | Possible formation of a pore less mud, possible P deficiency, rockiness, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| CNd | Eroded soil, medium to heavy texture, black, yellowish or olive, sometimes mottled, shallow |  | Hillsides and intermediate mountain areas. |  |  | Clay-loam to clay Clay-loam to clay | 90 - 180 | 6.5 - 8.2 7.2 - 7.9 |  |  |  | Kastanozems and vertic Luvisols | Extremely high erosion risks, drainage necessary, unfavorable germination, Possible deficiency in Zn and Fe (high pH) | Deficiency of Fe when aerobic and Zn when anaerobic (high pH), sometimes topography sub-optimal |
| CNdp | Eroded soil, heavy texture, black, yellowish or olive, sometimes mottled, shallow and rocky | Clay deposits, non-consolidated. Plenty of rocks from several origins | Hillsides and intermediate mountain areas. | Savannah and degraded pastures | Flat to strongly undulated 0 - 15 | Sandy-clay-loam to clay Clay | 90 - 180 | 6.5 - 8.2 7.2 - 7.9 | 1.8 - 7.8 | Imperfectly drained to poorly drained | Pelluderts | Vertisols, Cambisols, Luvisols and vertic Kastanozems | Rockiness, extremely high erosion risks, drainage necessary, unfavorable germination, Possible deficiency in Zn and Fe (high pH) | Rockiness, possible formation of a pore less mud, possible P deficiency, rockiness, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH), sometimes sub-optimal topography |
| TN | Heavy textured soil, black or grayish-brown, moderately deep and stony | Lacustrine limestone and basic eruptive rocks | Plateaus | Forest, prairie and crops (vegetable gardens, fruit crops) | Flat to slightly undulating 0 - 3 | Clay Clay-loam to clay | 70 - 150 | 6.1 - 7.5 6.7 - 8.2 | 3.6 - 9.2 | Well drained to poorly drained |  | Vertisols | Rockiness, drainage needed, manual tilling difficult (vertic soil), possible deficiency in Zn and Fe (high pH) | Rockiness, possible formation of a pore less mud, possible P deficiency, rockiness, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| Lowlands and depressions in mountain areas (PCX, AS, PCC) |
| PCX | Heavy textured soil, brownish, grayish, deep | Dolomitic marl and limestone | Depression in mountain areas | Forest, groves, and crops (coffee, fruit trees and annual crops) | Undulated to hilly (3 - 30) | Clay-loam to clay Loamy to clay | >150 | 5.3 - 7.7 6.0 - 8.5 | 2.7 - 7.1 | sometimes very poorly drained, imperfectly drained to poorly drained | Chromusterts | Vertisols , vertic Gleysols | Drainage needed, manual tilling difficult (vertic soil), possible deficiency in Zn and Fe (high pH), sometimes low fertility | Possible formation of a pore less mud, possible P deficiency, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| PCXp | Heavy textured soil, brownish, grayish, deep and rocky |  | Depressions and hillsides in mountain areas |  |  |  |  |  |  | imperfectly drained to poorly drained |  | Vertisols, vertic Kastanozems, vertic Luvisols, vertic Cambisols | Rockiness, drainage needed, manual tilling difficult (vertic soil), possible deficiency in Zn and Fe (high pH) | Rockiness, possible formation of a pore less mud, possible P deficiency, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| PCXd | Heavy textured soil, brownish, grayish, shallow |  |  |  |  |  | 80 - 150 | 6.6 - 8.1 6.2 - 8.5 |  |  |  |  | Drainage needed, manual tilling difficult (vertic soil), possible deficiency in Zn and Fe (high pH) | Possible formation of a pore less mud, possible P deficiency, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| PCXdp | Heavy textured soil, brownish, grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, drainage needed, manual tilling difficult (vertic soil), possible deficiency in Zn and Fe (high pH) | Rockiness, possible formation of a pore less mud, possible P deficiency, excessive percolation when dry, deficiency of Fe when aerobic and Zn when anaerobic (high pH) |
| AS | Salty soil, medium to heavy texture, yellowish to grayish, moderately deep and mottled | Alluvial and colluvial material | Lowlands and saline depressions on the seashore | Cactuses or no vegetation | Flat 0 - 1 | Silty-clay-loam to clay Clay-loam to clay | 90 - 150 | 7.8 – 8 8 - 8.3 | 1.5 - 1.8 | Very poorly drained | Haplaquepts | Solonchaks, Solonetz | Salinity and Sodicity, drainage needed non adapted for rain fed agriculture), possible deficiency in Fe and Zn (high pH) | Salinity and Sodicity, drainage needed (non adapted for rain fed agriculture), possible deficiency in Fe and Zn (high pH) |
| PCC | Heavy textured soil, olive or grayish, moderately deep to very deep | Compact limestone and argilic-silicious rocks | Lowlands | Prairies | Flat to slightly undulated 0 - 3 | Clay Clay | > 50 | 7.9 - 8.9 7.6 - 8.6 | 2.5 - 4.0 | Poorly drained | Dystropepts | Kastanozems | Drainage needed, probable Zn and Fe deficiency (high pH), compaction risk when tilled while moist, low fertility | Possible formation of a pore less mud, deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility |
| PCCp | Heavy textured soil, olive or grayish, moderately deep to very deep, rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, drainage needed, probable Zn and Fe deficiency (high pH), compaction risk when tilled while moist, low fertility | Rockiness, possible formation of a pore less mud, deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility |
| PCCd | Heavy textured soil, olive or grayish, shallow |  |  |  |  |  | 0 - 50 |  |  |  |  | Lithosols | Soil depth, probable deficiency in Fe and Zn (high pH), compaction risk when tilled while moist, low fertility | Low or no potential due to soil depth |
| PCCdp | Heavy textured soil, olive or grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Soil depth, rockiness, probable Zn and Fe deficiency (high pH), compaction risk when tilled while moist, low fertility | Low or no potential due to soil depth |
| Hilly and mountainous areas (CX, PXG, PE, CLO, CEU, VX, PCR, CR, CZ, PA, PC, VCE, CMC, PG, VR, AR) |
| CX | Medium texture soil, yellowish, dull orange or brownish, very deep | Metamorphic schist | Plateaux and hillsides | Forests and crops (coffee and vegetable gardens) | Slightly undulated to strongly undulated 1 - 15 | Sandy loam to clay Sandy-loam to clay | >180 | 5.1 - 6.5 5.2 - 7.0 | 3.0 - 6.4 | Rarely poorly drained, well drained to imperfectly drained | Humitropepts | Cambisols, Luvisols, Acrisols | Liming necessary for crops sensitive to soil acidity, low fertility, sometimes drainage needed | Compaction risk, sub-optimal infiltration, low fertility, sometimes Al toxicity in aerobic soil layers |
| CXd | Medium texture soil, yellowish, dull orange or brownish, shallow |  |  |  |  |  | 30 - 180 |  |  |  |  |  |  |  |
| CXdp | Medium texture soil, yellowish, dull orange or brownish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, liming necessary for crops sensitive to soil acidity, low fertility, sometimes soil limiting depth and liming necessary for all crops | Rockiness, compaction risk, sub-optimal infiltration, low fertility, sometimes Al toxicity in aerobic soil layers, soil depth |
| PXG | Medium to heavy textured soil, yellowish or grayish, deep | Argilic schist and micaceous sandstone | Mountains and hills | Forests and crops (coffee and vegetable gardens) |  | Sandy-loam to clay Sandy-loam to clay-loam | >150 | 5.1 - 6.8 5.1 - 6.9 | 2.7 - 6 | Imperfectly drained to poorly drained | Haplustolls | Cambisols, Kastanozems | Compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, sub-optimal drainage or sometimes drainage necessary, low fertility, sometimes unfavorable to germination | Compaction risk, low fertility, sometimes sub-optimal infiltration and Al toxicity in aerobic soil layers |
| PXGp | Medium to heavy textured soil, yellowish or grayish, rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, sub-optimal drainage or sometimes drainage necessary, low fertility, sometimes unfavorable to germination | Rockiness, compaction risk, low fertility, sometimes sub-optimal infiltration and Al toxicity in aerobic soil layers |
| PXGd | Medium to heavy textured soil, yellowish or grayish, shallow |  |  |  |  |  | 50 - 150 |  |  |  |  |  | Erosion risk and compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, sub-optimal drainage or sometimes drainage necessary, low fertility, sometimes unfavorable to germination | Sometimes limiting soil depth, sub-optimal topography |
| PXGdp | Medium to heavy textured soil, yellowish or grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, Erosion risk and compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, sub-optimal drainage or sometimes drainage necessary, low fertility, sometimes unfavorable to germination | Rockiness and sometimes limiting soil depth, sub-optimal topography |
| PE | Medium to heavy textured soil, yellowish to reddish, deep | Basalt, dolerite and volcanic tuff | Plateaus | Forests and groves | Flat to undulated 0 - 8 | Sandy-clay-loam to clay Sandy-loam | >150 | 4.9 - 6.9 5.4 - 6.5 | 2.4 - 12 | Well drained | Troporthents | Cambisols, Luvisols | Low fertility, sometimes unfavorable to germination and liming necessary | Sub-optimal infiltration, compaction risk, low fertility |
| PEd | Medium to heavy textured soil, yellowish to reddish, shallow |  | Plateaus' slopes with rock outcrops |  | Strongly undulated to mountainous >8 | Sandy-loam to sandy-clay-loam Sandy-clay-loam to clay-loam | 20 - 150 |  |  |  |  | Lithosols, Luvisols, Regosols | Erosion risk high, low fertility, sometimes unfavorable to germination and liming necessary | Low or no potential due to rock outcrops and sometimes inadequate topography , soil depth, rockiness |
| PEdp | Medium to heavy textured soil, yellowish to reddish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, Erosion risk high, low fertility, sometimes unfavorable to germination and liming necessary |  |
| CLO | Heavy textured soil, red and very deep | Schist with acidic rocks inclusions (gneiss, diorite) and basic rock inclusions (gabbros, basalt and pyroxenit) | plateaux | Forest and coffee | Flat to undulated 0 - 8 | Clay Clay | >100 | 5.7 - 7.4 5.6 - 7.5 | 2.1 - 4.3 | Well drained to imperfectly drained | Haplustolls | rodic Ferralsols | compaction risk when tilled while moist liming necessary for crops sensitive to soil acidity, low fertility | Possible formation of a pore less mud, low fertility |
| CLOp | Heavy textured soil, red and very deep, rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, low fertility | Rockiness, possible formation of a pore less mud, low fertility |
| CLOd | Heavy textured soil, yellowish to brownish, shallow |  | Hillsides and mountains |  | Strongly undulated to mountainous >8 | Sandy-loam to clay Sandy-loam to clay | 30 - 100 |  |  | Well drained to excessively drained |  | Cambisols, Lithosols | Soil depth, compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, low fertility | Inadequate topography and soil depth, possible formation of a pore less mud, low fertility |
| CLOdp | Heavy textured soil, yellowish to brownish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, soil depth, compaction risk when tilled while moist, liming necessary for crops sensitive to soil acidity, low fertility | Inadequate topography , rockiness, soil depth, possible formation of a pore less mud, low fertility |
| CEU | Heavy textured soil, yellowish to grayish or olive, very deep | schist and sandstones | Plateaux | Forests and groves | Flat to undulated 0 - 8 | Clay Clay | >150 | 6.0 - 7.7 6.5 - 8.0 | 1.3 - 4.4 | Imperfectly drained to poorly drained | Haplustolls | Luvisols, Cambisols, Kastanozems | Sub-optimal drainage, low fertility, compaction risk when tilled while moist | Possible formation of a pore less mud, low fertility |
| CEUp | Heavy textured soil, yellowish to grayish or olive, very deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, sub-optimal drainage, low fertility, compaction risk when tilled while moist | Rockiness, possible formation of a pore less mud, low fertility |
| CEUd | Heavy textured soil, yellowish to grayish or olive, shallow |  | Plateaus’ slopes |  | Strongly undulated to mountainous >8 | Sandy-loam to clay Sandy-clay-loam to clay | 50 - 150 |  |  |  |  |  | Low water holding capacity, erosion risk, low fertility, compaction risk when tilled while moist | Inadequate topography , possible formation of a pore less mud, low fertility |
| CEUdp | Heavy textured soil, yellowish to grayish or olive, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, low water holding capacity, erosion risk, low fertility, compaction risk when tilled while moist | Inadequate topography , rockiness, possible formation of a pore less mud, low fertility |
| VX | Medium to heavy textured soil, red, very deep | Schist | Plateaus and nearby hillsides | Forest and coffee | Flat to undulated 0 - 8 | Sandy-clay-loam to clay Sandy-clay-loam to clay | >150 | 5 - 6.2 5.3 - 6.1 | 2.4 - 7 | Well drained | Xerochrepts | chromic Cambisols, orthic and ferric Acrisols, chromic and orthic Luvisols | Compaction risk when tilled while moist, low fertility, liming necessary for crops sensitive to soil acidity, sometimes P fixation risk (possible deficiency) | Possible formation of a pore less mud, Al toxicity in aerobic soil layers, low fertility, sometimes compaction risk, sometimes P fixation risk (possible deficiency) with Fe toxicity |
| VXp | Medium to heavy textured soil, red, very deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, low fertility, liming necessary, sometimes P fixation risk (possible deficiency) | Rockiness, possible formation of a pore less mud, Al toxicity in aerobic soil layers, low fertility, sometimes compaction risk, sometimes P fixation risk (possible deficiency) |
| VXd | Medium to heavy textured soil, red, shallow |  |  |  | strongly undulated to steep slopes 8 -45 |  | 30 - 150 |  |  |  |  | chromic Cambisols, ferric Acrisols, Lithosols | Erosion risk high, compaction risk when tilled while moist, low fertility, liming necessary | Inadequate topography , possible formation of a pore less mud Al toxicity in aerobic soil layers, low fertility, sometimes compaction risk and limiting soil depth |
| VXdp | Medium to heavy textured soil, red, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk, rockiness, compaction risk when tilled while moist, low fertility, liming necessary | Inadequate topography , rockiness, possible formation of a pore less mud, Al toxicity in aerobic soil layers, low fertility, sometimes compaction risk and limiting soil depth |
| PCR | Medium to heavy textured soil, grayish and very deep | Coralliferous limestone | Terraces and hills | Savannah and sometimes crops (vegetable gardens and fruit trees) | Flat to undulated 0 - 8 | Silty-loam to clay Silty-loam to clay | >150 | 7.1 – 8 6.8 - 8.3 | 2.7 - 9 | Well drained to imperfectly drained | Eutrocepts | Cambisols | Compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility |
| PCRp | Medium to heavy textured soil, grayish, very deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Rockiness, possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility |
| PCRd | Medium to heavy textured soil, grayish and shallow | Coralliferous limestone | Terraces and hills | Savannah and sometimes crops (vegetable gardens and fruit trees) | Strongly undulated 8 - 15 | Silty-loam to clay Silty-loam to clay | 30 - 150 | 7.1 – 8 6.8 - 8.3 | 7.1 – 8 6.8 - 8.3 | Well drained to imperfectly drained | Eutrocepts | Cambisols | Erosion risk, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH), sometimes limiting soil depth | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, sometimes soil depth |
| PCRdp | Medium to heavy textured soil, grayish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk, rockiness, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH), sometimes limiting soil depth | Possible formation of a pore less mud, rockiness, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, sometimes limiting depth and sub-optimal topography |
| CR | Medium to heavy textured soil, black or yellowish, rocky and very deep | Coralliferous limestone and sandstone | hills top | savannah and prairies | Flat to undulated 0 - 8 | Clay-loam to clay Clay-loam to clay | >15 | 7.4 - 8.3 7.9 - 8.8 | 3.2 - 9 | Well drained to imperfectly drained | Calciustolls | calcaric Cambisols, calcaric Vertisols, calcaric Regosols | Compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH), sometimes difficult to till manually while dry (vertic soil) | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, sometimes risk of cracking strongly when dry and possible P deficiency |
| CRd | Medium to heavy textured soil, black or yellowish, rocky and shallow |  | hillsides |  | strongly undulated to hilly 8 - 30 |  | 50 - 150 |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH), sometimes difficult to till manually while dry (vertic soil) | Rockiness, possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, sometimes risk of cracking strongly when dry and possible P deficiency, limiting depth |
| CZ | Heavy textured eroded soil, brownish to dull orange, very deep | Limestone and calcareous marl | hills top | Savannah and prairies | Flat to undulated 0 - 8 | Clay Clay | >150 | 7.4 - 8.3 7.9 - 8.8 | 1.4 - 5.2 | Imperfectly drained to poorly drained | Calciustolls | calcaric Cambisols, calcaric Vertisols, calcaric Regosols | Erosion risk and compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH) |
| CZd | Heavy textured eroded soil, brownish to dull orange, shallow |  | hillsides |  | Strongly undulated to hilly 8 - 30 |  | 50 - 150 |  |  |  |  |  | Erosion risk extremely high, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), sometimes limiting depth |
| CZdp | Heavy textured eroded soil, brownish to dull orange, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk extremely high, rockiness, compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Rockiness, possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), sometimes limiting depth |
| PA | Heavy textured soil, yellowish to dull orange, very deep | Clays mixed with coralliferous limestone | Plateaux | Savannah and crops | Flat to slightly undulated 0 - 3 | Clay-loam to clay Clay | >150 | 8.1 - 8.5 6.0 - 8.5 | 2.6 - 3 | Poorly drained | Calciustolls | calcaric Cambisols, calcaric Regosols | Compaction risk when tilled while moist, low fertility, and probable Zn and Fe deficiency (high pH) | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility |
| PC | Medium textured soils, yellowish, deep | Limestone | Slopes | not specified | strongly undulated to hilly 8 - 30 | Loam Clay | >100 | 7.3 - 8.3 7.7 - 8.7 | 3 - 6.0 | Well drained | Dystropepts | Cambisols | Erosion risk, low fertility, unfavorable to germination, and probable Zn and Fe deficiency (high pH) | Low fertility, compaction risk, inadequate topography |
| PCd | Medium textured soils, yellowish, shallow |  |  |  |  |  | 10 - 100 |  |  |  |  | Cambisols, Lithosols | Erosion risk high, limiting depth, and probable Zn and Fe deficiency (high pH) | Low or no potential due to limiting depth and inadequate topography |
| PCdp | Medium textured soils, yellowish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk high, limiting depth, rockiness, and probable Zn and Fe deficiency (high pH) | Low or no potential due to limiting depth, inadequate topography inadequate topography and rockiness |
| VCe | Heavy texture soil, red, shallow or moderately deep and rocky | Rose limestone associated with eruptive rocks | Hillsides | Groves and prairies | strongly undulated to hilly 8 - 30 | Clay Clay | 8 - 150 | 7.3 - 7.6 6.4 - 7.8 | 6-Mar | well drained | Xerochrepts | chromic Cambisols, chromic Luvisols | Compaction risk when tilled while moist, low fertility, sometimes Zn and Fe deficiency (high pH) | Possible formation of a pore less mud, low fertility, sometimes and deficiency in Fe when aerobic and Zn when anaerobic (high pH) |
| CMC | Heavy textured soil, olive or yellowish, deep | Marl and limestone | Hillsides | savannah and groves | flat to hilly 0 - 30 | Clay Silty-clay to clay | >100 | 7.5 - 8.1 7.8 - 8.4 | 0.8 - 4.5 | Imperfectly drained to poorly drained | Calcustolls | vertic Cambisols, calcaric Regosols, Rendzinas | Compaction risk when tilled while moist, low fertility, sub-optimal drainage, and probable Zn and Fe deficiency (high pH), sometimes erosion risk | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, sometimes inadequate topography |
| CMCp | Heavy textured soil, olive or yellowish, deep and rocky | Marl and limestone | Hillsides | Savannah and groves | flat to hilly 0 - 30 | Clay Silty-clay to clay | >100 | 7.5 - 8.1 7.8 - 8.4 | 0.8 - 4.5 | Imperfectly drained to poorly drained | Calcustolls | vertic Cambisols, calcaric Regosols, Rendzinas | Rockiness, compaction risk when tilled while moist, low fertility, sub-optimal drainage, and probable Zn and Fe deficiency (high pH), sometimes erosion risk | Rockiness, possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, no potential when inadequate topography |
| CMCd | Heavy textured soil, olive or yellowish, shallow |  |  |  |  |  | 30 - 100 |  |  |  |  |  | Compaction risk when tilled while moist, low fertility, sub-optimal drainage, and probable Zn and Fe deficiency (high pH), sometimes erosion risk | Possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, no potential when inadequate topography |
| CMCdp | Heavy textured soil, olive or yellowish, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, low fertility, sub-optimal drainage, and probable Zn and Fe deficiency (high pH), sometimes erosion risk | Rockiness, possible formation of a pore less mud, and deficiency in Fe when aerobic and Zn when anaerobic (high pH), low fertility, no potential when inadequate topography |
| PG | Medium textured soil, variable colors, deep | Micaceous sandstone | Plateaux and hillsides | prairies | Flat to slightly undulated 0 - 3 | Clay-loam Clay-loam to clay | >100 | 5.0 - 5.2 5.5 - 6.0 | 4.6 - 6.4 | Imperfectly drained to poorly drained | Eutrocepts | Cambisols, Kastanozems | Erosion risk high, sub-optimal drainage, liming, low fertility | Compaction risk, low fertility |
| PGp | Medium textured soil, variable colors, deep and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk high, rockiness, sub-optimal drainage, liming necessary for crops sensitive to soil acidity, low fertility | Rockiness, compaction risk, low fertility |
| PGd | Medium textured soil, variable colors, shallow |  | Plateaux and hillsides |  | strongly undulated to hilly 8 - 30 |  | 50 - 100 |  |  |  |  |  | Erosion risk very high, liming necessary for crops sensitive to soil acidity, low fertility | Low or no potential due to topography and soil depth |
| PGdp | Medium textured soil, variable colors, shallow and rocky |  |  |  |  |  |  |  |  |  |  |  | Erosion risk very high, rockiness, liming necessary for crops sensitive to soil acidity, low fertility |  |
| VR | Brownish or red soil, variable depth, sometimes with concretions | Coralliferous limestone and calcareous conglomerate | Plateaux | Forest or savannah | Flat to undulated 0 - 8 | Clay Clay | >50 | 5.7 - 7.6 5.7 - 7.5 | 3.1 - 10 | Well drained to imperfectly drained | Humitropepts | chromic and ferric Luvisols, rodic Ferralsols, ferric Acrisols | Compaction risk when tilled while moist, probably P fixation (low availability), low fertility, liming necessary, Al toxicity risk | Possible formation of a pore less mud, likely P deficiency, Fe toxicity, low fertility |
| VRp | Brownish or red soil, variable depth, sometimes with concretions, rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, probably P fixation (low availability), low fertility, liming necessary, Al toxicity risk | Rockiness, possible formation of a pore less mud, likely P deficiency, Fe toxicity, low fertility |
| VRd | Brownish or red soil, shallow, sometimes with concretions |  |  |  | Flat to strongly undulated 0 - 15 | Clay Bedrock or clay | <50 |  |  |  | Haplustalfs, Tropudults | Rendzinas, calcaric Regosols, calcaric Lithosols | Erosion risk, compaction risk when tilled while moist, probably P fixation (low availability), low fertility, liming necessary, Al toxicity risk | Low or no potential due to limiting depth, sometimes rockiness and sub-optimal topography |
| VRdp | Brownish or red soil, shallow, sometimes with concretions and rocky |  |  |  |  |  |  |  |  |  |  |  | Rockiness, compaction risk when tilled while moist, probably P fixation (low availability), low fertility, liming necessary, Al toxicity risk |  |
| AR | See above (soils VR) |  |  |  | See above (soils VR) |

| Soil´s complexes |
| --- |
| Symbol | Estimation | 70% | 60% | 55% | 50% | 40% | 30% | 20% | 15% | 10% | Soils aptitude (see individual soil associations) |
| A3H | G+Ap+Am+Alp |  |  |  | G |  |  | Ap,Am |  | Alp |  |
| ABH | Am+Ap+Aph+BCp+BCm+BClp |  |  |  |  |  | Am | Ap,Aph |  | BCp,BCm,BClp |  |
| ACVR | Apc+Amc+VR |  |  |  |  | Apc | Amc,VR |  |  |  |  |
| ATA | Am+Alp+Aph+Ath+At |  |  |  |  |  | Am | Alp,At,Ath |  | Aph |  |
| ATBA | BC+At+Atd+Atdp |  |  |  | BC |  | At |  |  | Atd,Atdp |  |
| ATC | Apc+Alc+Atpc+Atdc+Atec |  |  |  |  |  | Apc | Alc,Atpc |  | Atdc,Atec |  |
| ATPG | At+PXG+PXGd+Atd+Atdp |  |  |  |  |  | At,PXG | PXGd |  | Atd,Atdp |  |
| ATVX | At+PCX+PXG+Atd+Atdp+PCXd+PXGd |  |  |  |  |  | At,VX |  |  | Atd,Atdp,VXd,VXdp |  |
| BA | Am+BCm+Al+Alp+Ap+BCl+BClp+BCp |  |  |  |  |  |  | Am,BCm |  | Al,Alp,Ap,BCl,BClp,BCp |  |
| BAC | BCpc+BCmc+Apc+Amc+Alcp |  |  |  |  | BCpc |  | BCmc,Apc |  | Amc,Alcp |  |
| BACH | Amc+Apch+Apc+BCmc+BCpc |  |  |  |  |  | Amc,Apch | Apc |  | BCmc,BCpc |  |
| BACP | Apc+BCpc+PCC+Amc+Alcp+BCmc+PCCd |  |  |  |  |  |  | Apc,BCpc,PCC |  | Amc,Alp,BCmc,PCCd |  |
| BACZ | Apc+BCpc+CZ+Amc+Alcp+BCmc+CZd |  |  |  |  |  |  | Apc,BCpc,CZ |  | Amc,Alp,BCmc,CZd |  |
| BCTC | BCmc+BClcp+Atdc+Atc+BClc |  |  |  |  |  | BCmc | BClcp,Atp,Atd |  | BClc |  |
| CAT | Atdp+Atd+Ate+Atdpc | Atdp |  |  |  |  |  |  |  | Atd,Ate,Atcdpc |  |
| CECN | CE+CN+CNd+CEd |  |  |  |  | CE | CN | CNd |  | CEd |  |
| CEPE | CE+PE+CEd+CEp+PEd+PEp |  |  |  |  |  | CE,PE |  |  | CEd,CEp,PEd,PEp |  |
| CLCF | CLOp+CFDp+CFDd+CLO+CLOd |  |  |  |  |  | CLOp,CFDp |  |  | CLOd,CLO,CFDd,CFD |  |
| CLCM | CLOp+CMCp+CLOd+CMC+CMCd |  |  |  |  |  | CLOp | CLOd,CMCp |  | CLO,CMCd,CMC |  |
| CLPE | CLOp+CLOd+PEp+PE+PEd+CLO |  |  |  |  |  | CLOp | CLOd,PEp |  | CLO,PEd,PE |  |
| CMCN | CMC+CN+CMCd+CNd+CNp |  |  |  |  |  | CMC,CN | CMCd |  | CNd,CNp |  |
| CMCZ | CMC+CZ+CMCd+CZd |  |  |  |  | CMC,CZ |  |  |  | CMCd,CZd |  |
| CMPC | CMC+PCC+CMCd+PCCd+PCCp |  |  |  |  | CMC | PCC |  |  | CMCd,PCCd,PCCp |  |
| CMPX | CMC+PCX+PCXd+CMCd |  |  |  |  | CMC | PCX | PCXd |  | CMCd |  |
| CMVR | VR+CMC+CMCd+VRd |  |  |  |  |  | CMC,VR | CMCd |  | VRd,VRp |  |
| CNCD | CN+CD+CNd+CDd |  |  |  | CN |  | CD |  |  | CNd,CDd |  |
| CNEU | CN+CNp+CEUp+CEU+CEUd |  |  |  |  |  | CN | CNp,CEUp |  | CNd,CEU,CEUd |  |
| CNPE | CN+PE+CNd+PEd |  |  |  | CN |  | PE |  |  | CDd,PEd |  |
| CNPG | CN+PXG+CNd+PXGd |  |  |  |  | CN,PXG |  |  |  | CNd,PXGd |  |
| CNVR | CN+CNd+VRd+VR |  |  |  | CN |  |  | CNd,VRd |  | VR |  |
| CPL | PA+VR+VRd+CZ |  | PA |  |  |  |  | VR |  | CZ,VRd |  |
| CPVR | CN+PC+VR+CNd+VRd |  |  |  |  |  | CN,PC | VR |  | CDd,VRd |  |
| CXVX | CX+VX+CXd+CXp+VXd+VXp |  |  |  |  |  | CX,VX |  |  | CXd,CXp,VXd,VXp |  |
| CZCN | CZ+CN+CZd+CNd |  |  |  |  | CZ,CN |  |  |  | CZd,CNd |  |
| PCCN | PCC+CN+CNd+PCCp+PCCd |  |  |  |  |  | PCC,CN | CNd |  | PCCd,PCCp |  |
| PCCZ | CZ+PCC+CZd+PCCd+PCCp |  |  |  |  |  | PCC,CZ | CZd |  | PCCd,PCCp |  |
| PCNM | PCC+PCCd+PCCp+CN+CMC+CNd+CNp+CMCd+CMCp |  |  |  |  |  |  | PCC |  | PCCd,PCCp,CN,CNd,CNp,CMCd,CMCp |  |
| PGCN | CN+PG+CNd+CNp |  |  |  |  | CN,PG |  |  |  | CNd,CNp |  |
| PGPX | PXG+PCX+PXGd+PCXd+PCXp |  |  |  |  |  | PXG | PG,PCX |  | PXGd,PCXd,PCXp |  |
| PXAP | PXG+Ap |  |  |  | Ap,PXG |  |  |  |  |  |  |
| PXCN | CN+PCX+CNd+PCXd |  |  |  | CN |  |  | CDd,PCX |  | PCXd |  |
| PXEU | PCX+CEU+PCXp+CEUp |  |  |  |  | PCX,CEU |  |  |  | PCXp,CEUp |  |
| PXNR | PCX+CN+VR+PCXd+CNd+VRd |  |  |  |  |  | PCX | CNd,VRd |  | PCXd,CN,VR |  |
| PXPC | PCX+PCXp+PCCp+PCXd+PCC+PCCd |  |  |  |  |  | PCX | PCXp,PCCp |  | PCXd,PCC,PCCd |  |
| PXPE | PXG+PE+PXGd+PEd+PEp |  |  |  |  |  | PXG | PXGd |  | PEd,PEp |  |
| PXPG | PXG+PCX+PXGd+PXGp+PCXd+PCXp |  |  |  |  | PXG |  | PCX |  | PXGd,PXGp,PCXd,PCXp |  |
| PXVR | PXG+VRd+VR |  |  | PXG |  |  | VRd |  | VR |  |  |
| TCCN | Atc+CN+Atdc+Atdcp+CNd |  |  |  |  |  | Atc,CN | Atcd |  | Atdpc,CDd |  |
| TCCZ | Atc+CZ+Atdc+Atdpc+CZd |  |  |  |  |  | Atc,CZ | Atdc |  | Atdpc,CZd |  |
| TCMC | Atc+CMC+Atdc+Atdpc+CMCd |  |  |  |  |  | Atc,CMC | Atcd |  | Atdpc,CMCd |  |
| TCME | Atc+CMC+PE+Atdc+Atdpc+CMCd+PEd |  |  |  |  |  |  | Atc,CMC,PE |  | Atdc,Atdpc,CMCd,PEd |  |
| TCMR | Atc+CMC+VR+Atdc+Atdpc+CMCd+VRd |  |  |  |  |  |  | Atc,CMC,VR |  | Atdc,Atdpc,CMCd,VRd |  |
| TCPG | Atc+PXG+Atdc+Atdpc+PXGd |  |  |  |  |  | Atc,PXG | Atdc |  | Atdpc,P0XGd |  |
| TCPR | Atc+Atdpc+PCRd+PCRdp+Atdc+PCR |  |  |  |  |  |  | Atc,Atdpc,PCRd,PCRdp |  | Atdc,PCR |  |
| TCVR | Atc+VRd+Atdpc+VR+CR+CRd |  |  |  |  |  | Atc | Atdpc,VRd |  | CR,CRd,VR |  |
| TVRZ | Atc+VRd+CZ+Atdc+Atdpc+VR+CZd |  |  |  |  |  |  | Atc,VRd,CZ |  | Atdpc,Atdc,VR,CZd |  |
| VCXU | VX+CX+VXdCXd+CEU+CEUd+CEUp |  |  |  |  |  | VX | CX |  | VXd,CXd,CEUd,CEUp,CEU |  |
| VRCZ | VR+CZ+CZd+VRd+VRp |  |  |  |  |  | VR,CZ | CZd |  | VRd,VRp |  |
| VRPC | VR+VRd+PCC+PCCd |  |  |  |  |  | VRd,VR,PCC |  |  | PCCd |  |
| VRPM | VRd+PCC+CMC+CMCd+PCCd |  |  |  |  | VRd |  | PCC,CMC |  | PCCd,CMCd |  |
| VRPX | VR+PCX+VRd+PCXd |  |  |  |  | VR | PCX | VRd |  | PCXd |  |
| VXCN | VX+CN+CNd+VXd+VXp |  |  |  |  |  | VX,CN | CNd |  | VXd,VXp |  |
| VXPG | VX+PXG+VXd+VXp+PXGd+PXGp |  |  |  |  |  | VX,PXG |  |  | VXd,VXp,PXGd,PXGp |  |

Methodology to assess soil association characteristics (source: “Os solos de Timor” – 1978):

- Source materials: As in publication

- Physiographic element: Most frequent elements

- Vegetation: As in publication

- Topography and slope: Most frequent values and elements

- Topsoil texture ( 0 – 20 cm): All textures

- Subsoil texture (20 – 60 cm): All textures

- Topsoil pH (0 – 20 cm): Average ± one standard deviation

- Subsoil pH ( 20 – 60 cm): Average ± one standard deviation

- Topsoil organic matter content: Average ± one standard deviation

- Drainage: Most frequent value

- FAO Soil classification: As in publication, USDA, Source: Ausaid

Soil aptitude:

Soil aptitude was determined for rain fed agriculture and irrigated rice culture, based on the Fertility Classification Capability version 3.5 (FCC). This is a theoretical aptitude.

All soil profiles described in Os Solos de Timor / The Soils of Timor were tested to determine the FCC profile classification (Annex 1 and 2).

The limitations for each soil association are the ones that are present with a frequency higher than 50%.

Aptitude limitations for rain fed agriculture:

- Not adapted for rain fed agriculture (FCC modifier “g”) – Defines wetland soils, only used for rain-fed agriculture in an intensive manner in short periods, using water resistant varieties. Prolonged saturation can induce Zn deficiency for irrigated rice culture.

- Rocky outcrops – Defines soils where rocky outcrops prevent the use of mechanized agriculture and reduce the soil’s potential to till with animal traction.

- Liming needed (FCC modifier “h”) – Defines soils with pH between 5 and 6 needing liming to acidic soil sensitive varieties, or the use of varieties that are adapted to acidic soils.

- Low water holding capacity – Defines sandy or sandy-loam soils (FCC modifier “S” or “SL) that store insufficient water.

- Deficient in Zn and Fe (FCC modifier “b”) – Defines calcareous soils with a pH superior to 7.4 within 60 cm depth, phosphate rock shouldn´t be used.

- Deficient in Fe when Aerobic and Zn when Anaerobic – for irrigated rice; see FCC modifier “b”.

- Drainage (FCC modifier “g”) – Defines soils that are moderately, imperfectly or poorly drained, water saturated during long periods, however do not have a significant impact on plants development.

- Low fertility (FCC modifier “k”) – Defines soils with low minerals availability, including K; K applications are necessary in small quantities, depending on soil chemical analysis results. For irrigated rice, K deficiency depends on the availability of K in the water.

- P-fixation (FCC modifier “i”) – P is poorly available, as is retained by clays. Apply phosphate once a year.

- Possible formation of a pore less mud – Defines clayey soils, (FCC modifier C or CC) used for irrigated rice crop and when tilled while moist or saturated.

- Low Cation Exchange Capacity (FCC modifier “e”) – Defines soils that can´t store large cation quantities, and need of small and periodic fertilization.

- Unfavorable to germination (FCC modifier “c”) – Defines soils with more than 30% silt in the topsoil, that lead to crust formation after the rain.

- Too rapid infiltration / sub-optimal infiltration: Defines soils with poor textures for irrigated rice crop, from Sandy to Loamy (FCC modifier “S” [sandy], “SL” [sandy over loamy], “L” [loamy] or “LS” [loamy over sandy]).

- Manual tilling difficult (FCC modifier “v”) – Defines soils with vertic properties (montmorillonite clays). These soils are very hard when dry.

- Rockiness – more than 15% rocks and/or grit with a diameter of 2 mm in the topsoil.

- Excessive percolation when dry (FCC modifier “v”) – defines with vertic properties. These soils absorb large quantities of water in the first stages of rice cultivation, possible P deficiency.

- Limiting depth – defines soils with bedrock within 60 cm depth and/or FCC modifier “R”.

- Compaction risks – Defines clayey soils (FCC modifier “C” or “CC”) in which porosity decreases substantially when tilled while moist.

- Erosion risks – Defines soils with bedrock within 30 cm depth and/or slopes superior do 8% and/or with an abrupt texture change within 60 cm depth, from Sandy to Clayey or from Loamy to Clayey FCC “SC” [sandy over clayey] or “LC” [loamy over clayey].

- Salinity and Sodicity – defines soils with an electrical conductivity over 4 mmhos/cm and N saturation higher than 15% within 1 meter depth. The content of soluble salts needs lixiviation with Ca salts to avoid particle dispersion.

- Inadequate physical support – defines organic soils that can’t bear agricultural machinery.

- Inadequate texture – See too rapid infiltration.

- Limiting topography / inadequate / sub-optimal – Defines slope’s suitability (>8% - sub-optimal; >15% - limiting; >30% - inadequate) for irrigated rice.

- Al Toxicity (FCC modifier “a”) – Defines soils with a pH < 5, liming is necessary for almost all crops.

Annex 1 – FCC Classification by mapping unit

| Symbol | FCC Classification | Profile Number | Symbol | FCC Classification | Profile Number | Symbol | FCC Classification | Profile Number | Symbol | FCC Classification | Profile Number |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Acl | LSbegk | 37 | BCcp | Cb | 460 | CRdp | Cbv | 631 | PEd | Lk | 428 |
| Acm | Lb | 40 | BCcp | Cbg | 329 | CRdp | Lbk | 64 | PEd | LLk | 625 |
| Acm | LLb | 54 | BCcp | Cbg | 331 | CX | LCak | 296 | PEdp | LLk | 413 |
| Acm | LLbgk | 114 | BCcp | Cbg | 626 | CX | LCg'hk | 316 | PEp | LLhk | 438 |
| Acp | Cbg | 121 | BCcphp | Cbg' | 632 | CX | Lg'k | 318 | PF | Chk | 641 |
| Acp | Cbg | 347 | BCcphp | CCbg' | 388 | CXd | Cak | 237 | PF | Ck | 621 |
| Acp | CCg | 341 | BCcphp | Cg' | 394 | CXd | LLghk | 229 | PF | CRhk | 642 |
| Al | Lbd | 21 | BCcphp | Cg' | 423 | CXdp | Lbgk | 269 | PF | LCgk | 327 |
| Al | Lg | 221 | BClp | LSgk | 498 | CXdp | Lhk | 186 | PG | LCghk | 603 |
| Al | Lgbk | 206 | BCm | L | 427 | CXdp | Lhk | 187 | PG | LCghk | 605 |
| Al | LLb | 288 | BCm | Lgk | 2054 | CXdp | LLgk | 180 | PXG | Cghk | 255 |
| Al | LSbgk | 12 | BCm | LLg | 629 | CXdp | LLhk | 233 | PXGd | Cbgk | 245 |
| Al | LSghk | 396 | BCm | LLk | 136 | CXp | CLak | 230 | PXGd | Cbgk | 346 |
| Al | LSgk | 19 | BCmp | Lbk | 38 | CXp | CLhk | 158 | PXGd | Cghk | 444 |
| Alp | LLgk | 287 | BCp | CCgv | 627 | CXp | LCbg'k | 279 | PXGd | Chk | 391 |
| Am | CC | 93 | BCp | Cg | 633 | CXp | LCg'hk | 207 | PXGd | CLghk | 297 |
| Am | Lbg | 8 | BCph | Cbg' | 634 | CXp | LChk | 164 | PXGd | CLghk | 604 |
| Am | LCh | 400 | BCphp | Cg' | 124 | CXp | Lhk | 272 | PXGd | LChk | 448 |
| Am | Lg | 20 | BCphp | Cg' | 390 | CZ | Ck | 140 | PXGd | LLagk | 247 |
| Am | Lg | 35 | CD | LLk | 624 | CZdp | Cbk | 157 | PXGdp | LLk | 299 |
| Am | Lgh | 9 | CD |  | 6 | G | Cbg'k | 634 | PXGp | Cgk | 148 |
| Am | Lgk | 227 | CE | Cak | 99 | G | Cbg'k | 2041 | PXGp | Lgk | 51 |
| Am | LLgk | 25 | Ced | LRk | 623 | G | Cbg'k | 2053 | RC | Lbk | 464 |
| Am | LLgk | 277 | CEp | Ck | 639 | G | CCbg'k | 61 | RC | LSbk | 2023 |
| Am | LSk | 193 | CEUd | Cbgk | 443 | G | Cg'k | 124 | RC | LSbk | 2036 |
| Ap | Cbg | 397 | CEUd | Chi | 387 | G | Lbg'k | 456 | TN | Cbgv | 630 |
| Ap | Cbg | 405 | CEUd | Ck | 454 | G | LLbg'k | 257 | TN | Cbgv | 2052 |
| Ap | CCgk | 301 | CEUd | LLgk | 33 | G | Cbg'k | 632 | TN | Cbgv | 2058 |
| Ap | Lbg | 11 | CEUdp | LLbgk | 39 | G | Lbg'k | 416 | TN | Cbg'v | 2055 |
| Ap | Lhgk | 417 | CEUp | Cbgk | 442 | G | LCg'k | 146 | TN | Cbv | 613 |
| App | CCbg | 132 | CLO | Chk | 437 | Gp | Cbg'k | 404 | TN | CCbgv | 353 |
| AR | - | - | CLO | Lh | 333 | Gp | Cbg'k | 426 | TN | Chv | 616 |
| AS | Cbg'ns | 2024 | CLOd | Cbk | 635 | Gp | CCbg'k | 293 | TN | CRbk | 107 |
| AS | CLbgns | 2035 | CLOp | Lk | 335 | Gp | CCbg'k | 388 | TN | CRk | 610 |
| Atclp | LSbgk | 127 | CMC | Cbgk | 418 | Gp | CCg'k | 423 | TNH | - | - |
| Atcp | Cbgk | 367 | CMCdp | Cbgk | 374 | Gp | Cg'k | 390 | TNHd | ORbgk | 612 |
| Atcp | CLbgk | 359 | CMCdp | CRbgk | 307 | Gp | Cg'k | 394 | VCe | Cbk | 618 |
| Atcp | LCbgk | 355 | CMCp | Cbgk | 370 | Gp | Cg'k | 410 | VCe | Ck | 617 |
| Atcpp | Cbgk | 118 | CMCp | Cbgv | 402 | Gp | CLbg'k | 470 | VR | Cak | 156 |
| Atl | L | 2056 | CN | Cbgv | 105 | PA | CCbk | 139 | VR | Cbgk | 80 |
| Atm | Lca | 103 | CN | Cbv | 643 | PA | CCbk | 145 | VR | Cbgv | 66 |
| Atm | Llhgk | 2047 | CN | Cgv | 378 | PCCp | Cbgk | 349 | VR | Cbik | 109 |
| Atmp | Lek | 26 | CNd | Cgv | 640 | PCd | LCbk | 622 | VR | Cbik | 113 |
| Atmp | Lhk | 24 | CNd | Lghk | 337 | PCR | Lbgk | 72 | VR | Chik | 85 |
| Atmp | LRagk | 439 | CNdp | Cbgv | 380 | PCRdp | Cbk | 110 | VR | Chik | 602 |
| Atp | Cg | 117 | CNdp | LCbgk | 303 | PCRp | Cbgk | 69 | VR | Chik | 614 |
| Atp | Cg | 2046 | CNp | Cbgv | 50 | PCX | Cghv | 381 | VR | Chk | 163 |
| Atp | Cga | 137 | CNp | Cbgv | 317 | PCX | LLghk | 494 | VR | Ck | 63 |
| Atp | Cga | 608 | CNp | Cbgv | 323 | PCXd | CRbgv | 619 | VR | Ck | 144 |
| Atp | Cgh | 149 | CNp | Cbgv | 325 | PCXdp | Cbv | 620 | VR | Ck | 425 |
| Atp | Cgh | 167 | CNp | Cbgv | 356 | PCXdp | CCbgv | 393 | VR | LChk | 150 |
| Atp | LC | 340 | CNp | Cbgv | 362 | PCXdp | Cgv | 375 | VR | ? | 135 |
| Atp | LCh | 338 | CNp | Cbgv | 376 | PCXdp | Chk | 377 | VRd | CRbik | 141 |
| Atp | LChgk | 336 | CNp | Cgv | 607 | PCXp | Cbgv | 92 | VRdp | CRk | 601 |
| BCcl | Lbeg' | 2048 | CNp | Chv | 153 | PCXp | Cbg'v | 126 | VRdp | LRbk | 135 |
| BCcl | SLb | 484 | CP | LRhk | 369 | PCXp | Cbg'v | 128 | VRp | Ck | 609 |
| BCcm | Lb | 458 | CPp | LRak | 371 | PCXp | Cbg'v | 130 | VX | Cagk | 200 |
| BCcm | Lb | 466 | CQ | LRhk | 606 | PCXp | LLak | 373 | VX | CCai | 179 |
| BCcm | Lb | 496 | CRd | Cbk | 637 | PCXpp | Cbgv | 56 | VX | Cghk | 199 |
| BCcm | LSb | 468 | CRd | Lbg | 345 | PE | Cak | 94 | VX | Chk | 192 |
| BCcmhp | Cbg' | 456 | CRdp | Cbgv | 636 | PE | LChk | 432 | VX | CLhik | 231 |
| VX | LCghk | 1 | VXd | LLk | 44 | VXp | CChk | 258 | VXp | Lhk | 324 |
| VX | LChk | 168 | VXdp | CRhk | 242 | VXp | Chk | 4 | VXp | LLak | 191 |
| VX | LChk | 306 | VXdp | LLhk | 178 | VXp | Chk | 260 | VXp | LLak | 290 |
| VX | Lk | 271 | VXdp | LLhk | 238 | VXp | CL | 197 | VXp | LLhk | 23 |
| VX | LLk | 280 | VXp | Cagk | 217 | VXp | CLghk | 292 | VXp | LLhk | 49 |
| VXd | Cagik | 183 | VXp | Cak | 216 | VXp | CLhk | 234 | VXp | LLhk | 172 |
| VXd | Cgh | 201 | VXp | Cak | 300 | VXp | LCk | 278 | VXp | LLhk | 256 |
| VXd | Chk | 328 | VXp | CCaik | 173 | VXp | Lhk | 17 | VXp | LLk | 32 |
| VXd | CLghk | 189 | VXp | CCaik | 209 | VXp | Lhk | 212 | VXp | LLk | 298 |
| VXd | LLhk | 218 | VXp | CCak | 510 |  |  |  |  |  |  |

Annex 2 – FCC Classification by profile

| Profile Number | Symbol | FCC Classification | Profile Number | Symbol | FCC Classification | Profile Number | Symbol | FCC Classification | Profile Number | Symbol | FCC Classification |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| 1 | VX | LCghk | 139 | PA | CCbk | 278 | VXp | LCk | 393 | PCXdp | CCbgv |
| 4 | VXp | Chk | 140 | CZ | Ck | 279 | CXp | LCbg'k | 394 | BCcphp | Cg' |
| 6 | CD | ? | 141 | VRd | CRbik | 280 | VX | LLk | 394 | Gp | Cg'k |
| 8 | Am | Lbg | 144 | VR | Ck | 287 | Alp | LLgk | 396 | Al | LSghk |
| 9 | Am | Lgh | 145 | PA | CCbk | 288 | Al | LLb | 397 | Ap | Cbg |
| 11 | Ap | Lbg | 146 | G | LCg'k | 290 | VXp | LLak | 400 | Am | LCh |
| 12 | Al | LSbgk | 148 | PXGp | Cgk | 292 | VXp | CLghk | 402 | CMCp | Cbgv |
| 17 | VXp | Lhk | 149 | Atp | Cgh | 293 | Gp | CCbg'k | 404 | Gp | Cbg'k |
| 19 | Al | LSgk | 150 | VR | LChk | 296 | CX | LCak | 405 | Ap | Cbg |
| 20 | Am | Lg | 153 | CNp | Chv | 297 | PXGd | CLghk | 410 | Gp | Cg'k |
| 21 | Al | Lbd | 156 | VR | Cak | 298 | VXp | LLk | 413 | PEdp | LLk |
| 23 | VXp | LLhk | 157 | CZdp | Cbk | 299 | PXGdp | LLk | 416 | G | Lbg'k |
| 24 | Atmp | Lhk | 158 | CXp | CLhk | 300 | VXp | Cak | 417 | Ap | Lhgk |
| 25 | Am | LLgk | 163 | VR | Chk | 301 | Ap | CCgk | 418 | CMC | Cbgk |
| 26 | Atmp | Lek | 164 | CXp | LChk | 303 | CNdp | LCbgk | 423 | Gp | CCg'k |
| 32 | VXp | LLk | 167 | Atp | Cgh | 306 | VX | LChk | 423 | BCcphp | Cg' |
| 33 | CEUd | LLgk | 168 | VX | LChk | 307 | CMCdp | CRbgk | 425 | VR | Ck |
| 35 | Am | Lg | 172 | VXp | LLhk | 316 | CX | LCg'hk | 426 | Gp | Cbg'k |
| 37 | Acl | LSbegk | 173 | VXp | CCaik | 317 | CNp | Cbgv | 427 | BCm | L |
| 38 | BCmp | Lbk | 178 | VXdp | LLhk | 318 | CX | Lg'k | 428 | PEd | Lk |
| 39 | CEUdp | LLbgk | 179 | VX | CCai | 323 | CNp | Cbgv | 432 | PE | LChk |
| 40 | Acm | Lb | 180 | CXdp | LLgk | 324 | VXp | Lhk | 437 | CLO | Chk |
| 44 | VXd | LLk | 183 | VXd | Cagik | 325 | CNp | Cbgv | 438 | PEp | LLhk |
| 49 | VXp | LLhk | 186 | CXdp | Lhk | 327 | PF | LCgk | 439 | Atmp | LRagk |
| 50 | CNp | Cbgv | 187 | CXdp | Lhk | 328 | VXd | Chk | 442 | CEUp | Cbgk |
| 51 | PXGp | Lgk | 189 | VXd | CLghk | 329 | BCcp | Cbg | 443 | CEUd | Cbgk |
| 54 | Acm | LLb | 191 | VXp | LLak | 331 | BCcp | Cbg | 444 | PXGd | Cghk |
| 56 | PCXpp | Cbgv | 192 | VX | Chk | 333 | CLO | Lh | 448 | PXGd | LChk |
| 61 | G | CCbg'k | 193 | Am | LSk | 335 | CLOp | Lk | 454 | CEUd | Ck |
| 63 | VR | Ck | 197 | VXp | CL | 336 | Atp | LChgk | 456 | BCcmhp | Cbg' |
| 64 | CRdp | Lbk | 199 | VX | Cghk | 337 | CNd | Lghk | 456 | G | Lbg'k |
| 66 | VR | Cbgv | 200 | VX | Cagk | 338 | Atp | LCh | 458 | BCcm | Lb |
| 69 | PCRp | Cbgk | 201 | VXd | Cgh | 340 | Atp | LC | 460 | BCcp | Cb |
| 72 | PCR | Lbgk | 206 | Al | Lgbk | 341 | Acp | CCg | 464 | RC | Lbk |
| 80 | VR | Cbgk | 207 | CXp | LCg'hk | 345 | CRd | Lbg | 466 | BCcm | Lb |
| 85 | VR | Chik | 209 | VXp | CCaik | 346 | PXGd | Cbgk | 468 | BCcm | LSb |
| 92 | PCXp | Cbgv | 212 | VXp | Lhk | 347 | Acp | Cbg | 470 | Gp | CLbg'k |
| 93 | Am | CC | 216 | VXp | Cak | 349 | PCCp | Cbgk | 484 | BCcl | SLb |
| 94 | PE | Cak | 217 | VXp | Cagk | 353 | TN | CCbgv | 494 | PCX | LLghk |
| 99 | CE | Cak | 218 | VXd | LLhk | 355 | Atcp | LCbgk | 496 | BCcm | Lb |
| 103 | Atm | Lca | 221 | Al | Lg | 356 | CNp | Cbgv | 498 | BClp | LSgk |
| 105 | CN | Cbgv | 227 | Am | Lgk | 359 | Atcp | CLbgk | 510 | VXp | CCak |
| 107 | TN | CRbk | 229 | CXd | LLghk | 362 | CNp | Cbgv | 601 | VRdp | CRk |
| 109 | VR | Cbik | 230 | CXp | CLak | 367 | Atcp | Cbgk | 602 | VR | Chik |
| 110 | PCRdp | Cbk | 231 | VX | CLhik | 369 | CP | LRhk | 603 | PG | LCghk |
| 113 | VR | Cbik | 233 | CXdp | LLhk | 370 | CMCp | Cbgk | 604 | PXGd | CLghk |
| 114 | Acm | LLbgk | 234 | VXp | CLhk | 371 | CPp | LRak | 605 | PG | LCghk |
| 117 | Atp | Cg | 237 | CXd | Cak | 373 | PCXp | LLak | 606 | CQ | LRhk |
| 118 | Atcpp | Cbgk | 238 | VXdp | LLhk | 374 | CMCdp | Cbgk | 607 | CNp | Cgv |
| 121 | Acp | Cbg | 242 | VXdp | CRhk | 375 | PCXdp | Cgv | 608 | Atp | Cga |
| 124 | BCphp | Cg' | 245 | PXGd | Cbgk | 376 | CNp | Cbgv | 609 | VRp | Ck |
| 124 | G | Cg'k | 247 | PXGd | LLagk | 377 | PCXdp | Chk | 610 | TN | CRk |
| 126 | PCXp | Cbg'v | 255 | PXG | Cghk | 378 | CN | Cgv | 612 | TNHd | ORbgk |
| 127 | Atclp | LSbgk | 256 | VXp | LLhk | 380 | CNdp | Cbgv | 613 | TN | Cbv |
| 128 | PCXp | Cbg'v | 257 | G | LLbg'k | 381 | PCX | Cghv | 614 | VR | Chik |
| 130 | PCXp | Cbg'v | 258 | VXp | CChk | 387 | CEUd | Chi | 616 | TN | Chv |
| 132 | App | CCbg | 260 | VXp | Chk | 388 | BCcphp | CCbg' | 617 | VCe | Ck |
| 135 | VRdp | LRbk | 269 | CXdp | Lbgk | 388 | Gp | CCbg'k | 618 | VCe | Cbk |
| 135 | VR | ? | 271 | VX | Lk | 390 | BCphp | Cg' | 619 | PCXd | CRbgv |
| 136 | BCm | LLk | 272 | CXp | Lhk | 390 | Gp | Cg'k | 620 | PCXdp | Cbv |
| 137 | Atp | Cga | 277 | Am | LLgk | 391 | PXGd | Chk | 621 | PF | Ck |
| 622 | PCd | LCbk | 632 | BCcphp | Cbg' | 640 | CNd | Cgv | 2046 | Atp | Cg |
| 623 | Ced | LRk | 632 | G | Cbg'k | 641 | PF | Chk | 2047 | Atm | Llhgk |
| 624 | CD | LLk | 633 | BCp | Cg | 642 | PF | CRhk | 2048 | BCcl | Lbeg' |
| 625 | PEd | LLk | 634 | BCph | Cbg' | 643 | CN | Cbv | 2052 | TN | Cbgv |
| 626 | BCcp | Cbg | 634 | G | Cbg'k | 2023 | RC | LSbk | 2053 | G | Cbg'k |
| 627 | BCp | CCgv | 635 | CLOd | Cbk | 2024 | AS | Cbg'ns | 2054 | BCm | Lgk |
| 629 | BCm | LLg | 636 | CRdp | Cbgv | 2035 | AS | CLbgns | 2055 | TN | Cbg'v |
| 630 | TN | Cbgv | 637 | CRd | Cbk | 2036 | RC | LSbk | 2056 | Atl | L |
| 631 | CRdp | Cbv | 639 | CEp | Ck | 2041 | G | Cbg'k | 2058 | TN | Cbgv |